## Slide 1: Embedded C++ Assessing OO concepts for Embedded Systems
Author: Fränz Ney (es16m013)
Supervisor: FH-Prof. Dipl.-Ing. Dr. Martin Horauer
13.11.2018

## Slide 2: Overview
Why using C++ in embedded projects?
What are the benefits of C++ over C?
Possible issues of C++.
Benchmark tests C++ vs C.
C++ memory overhead.

## Slide 3: C++ Concepts
Function Overloading
  Using the same function name for two or more functions.
Default Arguments
  Default value is used when the caller of the function doesn’t provide an argument.
Function Templates
  Developing functions independent from their data types.
Pointer vs References
  Safer alternative for pointers.

## Slide 4: C++ Standard Library
Pro
  Collection of classes and templates.
  Tested and documented algorithms can be used.
  Ease of use.
Contra
  Not transparent.
  Confusing Heap / Stack memory allocation.
  Can decrease system performance.

## Slide 5: C++ Concepts
Namespaces
  Increase the modularity of the code.
Classes
  Encapsulation of data.
  Access specifier (private, public, virtual).
Constructor / Destructor
  Always work with initialised data and modules.
Inheritance and Polymorphism
  Increase the modularity of the code.
  Using virtual functions or multiple inheritance could influence system performance.

## Slide 6: Benefits and Drawbacks
C++ Concept | Pro | Contra
Function Overloading |  | 
Default Arguments |  | 
Function Templates |  | 
Pointer vs References |  | 
C++ Standard Library |  | 
Namespaces |  | 
Classes |  | 
Constructor / Destructor |  | 
Inheritance and Polymorphism |  | 

## Slide 7: Ease of Use
C is simpler to learn than C++.
C++ requires more Know-How from the developer.
Debugging C++ programs could be difficult.
C Toolchain is available for the most platforms.

## Slide 8: Use cases
mbed-OS
distortos
StratifyOS
Kvasir
Modm
Crect
EMB2

## Slide 9: Questions

## Slide 10: Function Overloading
C++
C
int add_i(int a, int b){
return a + b;
}
double add_d(double a,double b){
return a + b;
}
int add(int a, int b){
return a + b;
}
double add(double a, double b){
return a + b;
}

## Slide 11: Default Arguments
C++
C
int uart_init(int baud=9600,
int Ndata=8){
return 0;
}
int uart_init(int baud,
int Ndata){
if(baud < 0)
baud = 9600;
if(Ndata < 0)
Ndata = 8;
return 0;
}

## Slide 12: Function Templates
C++
C
template <typename T> T add(T a, T b)
{
return a + b;
}
int add_i(int a, int b)
{
return a + b;
}
double add_d(double a, double b)
{
return a + b;
}

## Slide 13: Pointer vs References
int i = 3;
// A pointer to variable i (stores address of i)
int *ptr = &i;
// A reference (or alias) for i.
int &ref = i;

## Slide 14: C++ Standard Library (heap / stack confusing)
Code
Output
02: =
03: ==
:::
15: ==============
16: ===============
* Allocate 31 bytes
17: ================
18: =================
:::
30:=============================
31: ==============================
* Allocate 61 bytes
* Deallocate
32: ===============================
33: ================================
int main() {
std::string str;
for(int i=2; i <33; i++){
str.append("=");
printf("%02d: %s\n", i,
str.c_str());
}
return 0;
}

## Slide 15: Namespaces (anonym namespaces)
driver.cpp (API functions)
driver.cpp (internal usage)
namespace driver {
void serial_init(void){
is_init = INIT;
// Do something
}
void serial_send(char *data,
int len){
if(is_init == NOT_INIT)
return;
for(int i=0; i<len; i++)
send_byte(data[i]);
}
} //namespace driver
namespace {
typedef enum {INIT, NOT_INIT} state;
state is_init = NOT_INIT;
void send_byte(char byte){
// Do something
}
}

## Slide 16: Classes 1 (Basic Class ‘Com’)
class Com {
public:
void set_status(int status){
this->status = status;
};
int get_status(void){
return status;
};
virtual void send_byte(char byte){
printf("Com: %c \n", byte);
}
private:
int status;
};

## Slide 17: Classes 2 (Derived class ‘Serial’)
serial.cpp
serial.h
Serial::Serial(int _baud, int _mode)
: baudrate{_baud}, mode{_mode} {
buffer = new char[100];
}
Serial::~Serial(){
delete[] buffer;
}
void Serial::set_baudrate(int baudate){
this->baudrate = baudrate;
}
void Serial::set_mode(int mode){
this->mode = mode;
}
class Serial : public Com{
public:
Serial():Serial(9600, 1){};
Serial(int _baud, int _mode);
~Serial();
void set_baudrate(int baudate);
void set_mode(int mode);
private:
int baudrate;
int mode;
char *buffer;
};

## Slide 18: Classes 3 (Virtual Functions)
Class ‘Com’
Class ‘Serial’
class Com {
public:
void set_status(int status){
this->status = status;
};
int get_status(void){
return status;
};
virtual void send_byte(char byte){
printf("Com: %c \n", byte);
}
private:
int status;
};
class Serial : public Com{
public:
Serial():Serial(9600, 1){};
void set_baudrate(int baudate){};
void set_mode(int mode){};
void send_byte(char byte){
printf(“Serial: %c \n", byte);
}
private:
int baudrate;
int mode;
char *buffer;
};

## Slide 19: Classes 4 (Virtual Function Table)
void send(Com& arg) {
arg.send_byte('A');
}
int main(void){
Serial ser;
send(ser);
return 1;
}